## Slide 1: 김 덕 수 (Duksu Kim)
석·박사 통합과정, 전산과, KAIST
  2008/02 ~
  대용량 그래픽스 연구실
    지도교수: 윤성의
B.S., 정보통신 공학, 성균관 대학교
  2001/03 ~ 2008/02

## Slide 2: Proximity Computation on Heterogeneous Computing Systems
Duksu Kim
Advisor: Sung-Eui Yoon
Ph. D. Defense (20140520)

## Slide 3: Proximity Queries (PQs)
Compute relative placement or configuration of two objects
  Collision detection
  Distance computation
    Neighbor search
Basic operations in various applications
  Graphics, simulations,
  robotics, Etc.

## Slide 4: Proximity Queries in App.
Chart: 
| Others | Collision detection
Motion planning | 50 | 60
[Jia 2010] [Liangjun 2008]
Collision
detection
Motion planning
Realistic rendering
Chart: 
| Others | Ray-tracing
Realistic redering | 10 | 90
[Our in-house render]
Ray tracing
Particle-based Sim.
Chart: 
| Others | Neighbor search
Realistic redering | 20 | 80
Neighbor
search
[Our in-house simulator]

## Slide 5: Proximity Query Acceleration
Various acceleration techniques
  Acceleration hierarchies
  Culling algorithms
  Specialize algorithms for a target application
  Approximation algorithms
Achieve several orders of magnitude performance improvement

## Slide 6: Demands for High Performance
Takes few ~ tens or hundreds seconds
  for solving complex motion planning problem
  per frame for realistic rendering and particle simulations
Model complexity continue to grow for more realistic and accurate outputs
Motion planning
Realistic rendering
Particle-based Sim.

## Slide 7: Parallel Computing Trend
Multi/Many-core architectures
  Multi-core CPU
  Graphics processing unit (GPU)
Image from NVIDIA

## Slide 8: Parallel Computing Trend
Multi/Many-core architectures
Heterogeneous architectures
  Different types of computing devices in a system
    Multi-core CPUs and GPUs in a PC
  Intel Sandy Bridge, AMD Fusion, Sony Cell, ..
Images from NVIDIA

## Slide 9
[Lawlor 2002] [Ize 2007] [Wald 2007] [Tang 2009] [Lee 2010] [IABT 2011]
…
[Vassilev 2001] [Baciu 2002] [Govindaraju2005] [Govindaraju2005*] [Sud 2006] [HKK 2007] [Lauterbach 2010] [GSSP 2010]
…
Multi-core CPU
Proximity computation
GPU
Proximity computation
Achieve high performance improvement
Utilize either multi-core CPU or GPU
Do not provide interactive performance yet for large-scale models

## Slide 10
Multi-core CPU
Proximity computation
GPU
Proximity computation

## Slide 11
Multi-core CPU
Proximity computation
Proximity computation
Proximity computation
GPU

## Slide 12
Comp. Res. A
Comp. Res. C
Comp. Res. B
Comp. Res. D
Comp. Res. E
Proximity computation
Work distributor (Scheduler)
…

## Slide 13: Thesis Statement
We design systems that accelerate proximity computation for large-scale data by using heterogeneous computing resources
We maximize the utilization efficiency of heterogeneous systems by designing scheduling algorithms that consider the heterogeneity

## Slide 14: Approaches
Heterogeneous computing system for a specific proximity query
General proximity computing system and scheduling algorithm for a various proximity queries
Out-of-core proximity computation

## Slide 15: Outline
Introduction & Overview
Approaches
Conclusion

## Slide 16: Approaches
Heterogeneous computing system for a specific proximity query
General proximity computing system and scheduling algorithm for a various proximity queries
Out-of-core proximity computation

## Slide 17: HPCCD: Hybrid Parallel Continuous Collision Detection using CPUs and GPUs
Multi-core CPU
Hierarchical work
Elementary test
CCD
GPU
Duksu Kim, Jae-Pil Heo, JaeHyuk Huh, John Kim, Sung-Eui Yoon
Computer Graphics Forum (Pacific Graphics), 2009
Received a distinguished paper award at the conference

## Slide 18: Contributions
Utilize both multi-core CPUs and GPUs
  Workload distribution algorithm
  Efficient data communication technique
Propose a novel parallel continuous collision detection algorithm on multi-core CPUs

## Slide 19: Workload Distribution
CCD
Hierarchy update
Hierarchy traversal
Elementary test
(Tri-Tri intersection)

## Slide 20: Workload Distribution
Hierarchy update
Hierarchy traversal
Elementary test
(Tri-Tri intersection)
BVH update and traversal
Elementary tests
Multi-core CPUs
GPUs
Random accesses
- Branch prediction
- Caching
- Solving cubic equations
Streaming processors optimized with floating point operations

## Slide 21: Improve the Efficiency of Parallel Computing
BVH update and traversal
Elementary tests
Multi-core CPUs
GPUs
Synchronization free parallel hierarchy update and traversal
Data communication optimization
Remove synchronization in the main loop of continuous collision detection algorithm
Optimize data communication between CPU and GPU
Please see the thesis for the details

## Slide 22: Results
Testing Environment
  One quad-core CPU (Intel i7 CPU, 3.2 GHz )
  Two GPUs (NVIDIA GeForce GTX285)
  Run eight CPU threads by using Intel’s hyper threading technology
Compare the performance over using a single CPU-core

## Slide 23: Results
146K triangles
13.6 X speed-up
54ms (19 FPS)
94K triangles
10.4 X speed-up
23ms (43 FPS)
252K triangles
12.5 X speed-up
54ms (19 FPS)

## Slide 24: Results
94K triangles

## Slide 25: Limitations
Generality issue
  Specialize for CCD
No guarantee to efficient utilization of computing resource
  Manual workload distribution depending on the application-dependent heuristic

## Slide 26: Approaches
Heterogeneous computing system for a specific proximity query
General proximity computing system and scheduling algorithm for a various proximity queries
Out-of-core proximity computation

## Slide 27: Scheduling in Heterogeneous Computing Environments for Proximity Queries
Duksu Kim, Jinkyu Lee, Junghwan Lee, Insik Shin, John Kim, Sung-Eui Yoon
IEEE Transactions on Visualization and Computer Graphics, Sept., 2013
Selected as the Spotlight Paper for the issue
Comp. Res. A
Comp. Res. C
Comp. Res. B
Comp. Res. D
Comp. Res. E
Proximity computation
Optimization-based scheduling
…

## Slide 28: Contributions
Design a general heterogeneous computing framework for various proximity queries
Propose optimization-based scheduling algorithm
  Maximize the utilization efficiency of heterogeneous computing resources

## Slide 29: Overview
Proximity queries
Resource 1
Resource 2
Resource n
Optimization based job
scheduling
Hierarchical traversal
.
.
.
.
.
.
Common job types of
various proximity queries
Leaf-level computation

## Slide 30: Overview
Proximity queries
Resource 1
Resource 2
Resource n
Optimization based job
scheduling
Hierarchical traversal
.
.
.
.
.
.
Leaf-level computation

## Slide 31: Optimization-based Scheduling
Design an accurate performance model
  Predict how much computation time is required to finish jobs on a resource
  Important to achieve the optimal scheduling result
Expected running time model
Optimization formulation
Iterative LP solver

## Slide 32: Performance Model
Performance relationship between jobs and resources is complex
Job type 1
Job type n
Resource 1
Processor architecture
Memory
Communication
Execution model
…
Resource 2
Processor architecture
Memory
Communication
Execution model
…
…

## Slide 33: Performance Model
Abstract the complex relationship as an expected, linear model
Job type 1
Job type n
Resource 1
Processor architecture
Memory
Communication
Execution model
…
Resource 2
Processor architecture
Memory
Communication
Execution model
…
…
Expected, linear Running Time

## Slide 34: Performance Model
Running time is linearly increased as the number of jobs is increased

## Slide 35: Performance Model
Running time is linearly increased as the number of jobs is increased
Each computing resource requires a specific amount of setup cost

## Slide 36: Performance Model
Inter-device data transfer time depends on the pair of devices
Data transfer time is linearly increased as the number of jobs is increased

## Slide 37: Expected Running Time Model
T() : Expected running time on computing resource i for processing n jobs of job types j that are generated from computing resource k
Setup time
Processing time
Data transfer time

## Slide 38: Expected Running Time Model
Measure coefficients of our linear formulation for each proximity query with sample jobs
  The expected running time model shows high correlation (0.91 on average) with the observed data in tested benchmarks

## Slide 39: Optimization-based Scheduling
Formulate an optimization problem
  Based on the expected running time model
  Need to represent the scheduling problem as a form of optimization problem
Expected running time model
Optimization formulation
Iterative LP solver

## Slide 40: Optimization Formulation
Minimize the makespan (L) problem
Processing time
Processing time
Processing time
Processing time
CPU 1
CPU 2
GPU 1
GPU 2
Time
Computing
resource
Makespan (L)

## Slide 41: Optimization Formulation
Calculate the optimal job distribution with the expected running time
Resource i
Rest time for completing
already assigned jobs
Processing time for
jobs will be assigned
Expected processing time
The expected processing time of computing resources is equal or smaller than the makespan
①

## Slide 42: Optimization Formulation
Calculate the optimal job distribution with the expected running time
The expected processing time of computing resources is equal or smaller than the makespan
There are no missing or duplicated jobs
①
②

## Slide 43: Optimization Formulation
Calculate the optimal job distribution with the expected running time
The expected processing time of computing resources is equal or smaller than the makespan
There are no missing or duplicated jobs
Each job is atomic
Job distribution
①
②
③

## Slide 44: Optimization-based Scheduling
Expected running time model
Optimization formulation
Iterative LP solver

## Slide 45: Optimization-based Scheduling
High computational cost
  Jobs are dynamically generated at runtime
  Optimization process takes long time for interactive or real-time applications
Expected running time model
Optimization formulation
Iterative LP solver
NP-hard Problem!

## Slide 46: Optimization-based Scheduling
Expected running time model
Optimization formulation
Iterative LP solver
Positive floating-point numbers
Designed an iterative LP solving algorithm to handle the piece-wise condition
Please see the thesis for the details

## Slide 47: Results
Tested with various applications
  Simulations (Continuous collision detection)
  Motion planning (Discrete collision detection)
  Global illumination (Ray-Triangle intersection)

## Slide 48: Results
+GTX480
+GTX480
+GTX480
GTX480
Use same GPUs (low heterogeneity)
Continuous collision detection
Fracturing simulation
(252K Tri.)
Ours
Work stealing
(an well-known
algorithm for dynamic
workload distribution)
For conservative comparison, we did manual tuning to get the best performance for tested methods except for ours
FPS

## Slide 49: Results
FPS
+Tesla2075
+GTX480
+GTX580
+GTX285
Ours
Work stealing
Use different GPUs (high heterogeneity)
Continuous collision detection
Fracturing simulation
(252K Tri.)
For conservative comparison, we did manual tuning to get the best performance for tested methods except for ours

## Slide 50: Results
Motion planning
(137K Tri., 50K samples)
FPS
Ours
Work
stealing
Round-robin
FPS
Work
stealing
Round-robin
Ours
Use different GPUs
Use different GPUs
Global illumination
(436K Tri., 80M rays)
For conservative comparison, we did manual tuning to get the best performance for tested methods except for ours

## Slide 51: Limitation
Scheduling algorithm dose not consider the memory requirement for processing queries
  We assume that all computing resources have enough memory space

## Slide 52: Approaches
Heterogeneous computing system for a specific proximity query
General proximity computing system and scheduling algorithm for a various proximity queries
Out-of-core proximity computation
Improve computational efficiency for in-core algorithms

## Slide 53: Out-of-Core Proximity Computation for Particle-based Fluid Simulations
Duksu Kim, Myung-Bae Son, Young J. Kim, Jeong-Mo Hong, Sung-Eui Yoon
(To appear) Computer Graphics Forum (High Performance Graphics), July, 2014

## Slide 54: Motivation
To meet the higher realism, a large number of particles are required
  Tens of millions particles
In-core algorithm
  Manage all data in GPU’s video memory
  Can handle up to 5 M particles with 1 GB memory for particle-based fluid simulation
    [HKK 2007]
Recent commodity GPUs have 1 ~ 3 GB memories (up to 12 GB)

## Slide 55: Contributions
Propose out-of-core methods that utilize heterogeneous computing resources and processes neighbor search for a large number of particles
Propose memory footprint estimation method to identify a maximal work unit for efficient out-of-core processing

## Slide 56: Result
Up to 65.6 M Particles
Maximum data size: 13 GB
Ours
Map-GPU
NVIDIA mapped memory Tech.
- Map CPU memory space
into GPU memory address space
- Two hexa-core CPUs (192 GB Mem.)
- One GPU (3 GB Mem.)

## Slide 57: Particle-based Fluid Simulation
Neighbor search
Compute force
Move particles
ε
Performance bottleneck
- Takes 60~80% of simulation computation time
ε-Nearest Neighbor (ε-NN)

## Slide 58: Preliminary: Grid-based ε-NN
ε
(ε < )

## Slide 59: Preliminary: Grid-based ε-NN
(ε < )

## Slide 60: In-Core Algorithm (Data<Video Memory)
Main memory (CPU side)
GPU
Video memory
- Grid data
- Particle data
ε-NN
Results
Results
Assume:
Main memory is enough
- can equip up to 4 TB

## Slide 61: Data > Video Memory
Main memory (CPU side)
GPU
Video memory
- Grid data
- Particle data
ε-NN
Results
Results

## Slide 62: Out-of-Core Algorithm
Main memory (CPU side)
GPU
Video memory
- Sub-grid(Block) data
- Particle data
ε-NN
Results
Results

## Slide 63: Boundary Region
Required data in adjacent blocks
Inefficient to handle in out-of-core manner

## Slide 64: Boundary Region
Required data in adjacent blocks
Inefficient to handle in out-of-core manner
Multi-core CPUs handles the boundary region
  CPU (main) memory contain all required data
  Ratio of boundary region is usually much smaller than inner region

## Slide 65: How to Divide the Grid ?

## Slide 66: How to Divide the Grid ?
Goal: Find the largest block that fits to the GPU memory
  Improve parallel computing efficiency
    Processing a large number of particles at once
    Minimize data transfer overhead
  Reduce the boundary region
    As the ratio of boundary region is increased, the workload of CPU is increased

## Slide 67: Required Memory Size for processing a block, B
Data size
for storing a particle
Data size
for storing a neighbor info.
# of particles in B
# of neighbor particles
for the particle i (pi)

## Slide 68: Hierarchical Work Distribution
a
b
d
…
…
Front nodes
Workload tree
a
b
c
d
< GPU memory
c
- # of particles in the block
- # of neighbors in the block

## Slide 69: Chicken-and-Egg Problem
# of neighbor particles
for the particle i, pi
Data size
for storing a particle
Data size
for storing a neighbor info.
# of particles in B

## Slide 70: Chicken-and-Egg Problem
Our approach:
Estimation the number of neighbors for particles

## Slide 71: Problem Formulation
Assumption
  Particles are uniformly distributed in a cell
Idea
  For a particle, the number of neighbors in a cell is proportional to the overlap volume between the search sphere and the cell weighted by the number of particles in the cell
p
ε
S(p,ε)

## Slide 72: Expected Number of Neighbors of a particle p located at (x, y, z)
- : cells of and its adjacency cells
- : the number of particles in the cell
- : overlap volume between them
- : volume of the cell

## Slide 73: Problem Formulation
Compute for each particle takes high computational overhead
Instead, (approximation)
  Compute the average for particles in a cell
  Use the value for all particles in the cell

## Slide 74: The Average, Expected Number of Neighbors of particles in a cell
- is the length of a cell along each dimension
- is a particle positioned at (x, y, z) on a local coordinate space in
Expensive to compute at runtime

## Slide 75: The Average, Expected Number of Neighbors of particles in a cell

## Slide 76: The Average, Expected Number of Neighbors of particles in a cell
Pre-compute
  The value depends on the ratio between and values
  and are not frequently changed by user
  Use Monte-Carlo method with many samples (e.g., 1 M)
Use look-up table at runtime

## Slide 77: Validation
Correlation = 0.97
Root Mean Square Error (RMSE) = 3.7

## Slide 78: Chicken-and-Egg Problem
Expected number
of neighbors
Auxiliary space to cover the estimation error
RMSE

## Slide 79: Chicken-and-Egg Problem
Expected number
of neighbors
Auxiliary space to cover the estimation error
RMSE

## Slide 80: Results
Testing Environment
  Two hexa-core CPUs
  192 GB main memory (CPU side)
  One GPU (GeForce GTX 780) with 3 GB video memory

## Slide 81: Results
Up to 65.6 M Particles
Maximum data size: 13 GB
Ours
Map-GPU
NVIDIA mapped memory Tech
- Map CPU memory space
into GPU memory address space

## Slide 82
Up to 32.7 M Particles
Maximum data size: 16 GB
15.8 M Particles
Maximum data size: 6 GB

## Slide 83: Results
12 CPU cores
A CPU core
12 CPU cores
+One GPU
Map-GPU
Our method
Up to 26 X
Up to 51 X
Up to 8.4 X
Up to 6.3 X

## Slide 84: Outline
Introduction
Approaches
Conclusion

## Slide 85: Conclusion
We accelerate various proximity computation
  by efficiently utilizing heterogeneous computing resources
  With scheduling algorithm that considers heterogeneity of computing resources in computational and spatial perspective

## Slide 86: Future Work
General out-of-core techniques for various proximity queries
Extend our method to other applications

## Slide 87: Outcomes
3 Publications
  1 TVCG (SCI), 2 CGF (SCI-E)
6 Presentations
  3 conference talks (I3D, PG, GTC)
  3 conference poster (I3D, SIGGRAPH, HPG)
3 Patents, 1 SW package

## Slide 88: Publications
HPCCD: Hybrid Parallel Continuous Collision Detection using CPUs and GPUs
  Duksu Kim, Jae-Pil Heo, Jaehyuk Huh, John Kim, Sung-eui Yoon
  Computer Graphics Forum, Vol. 28, No. 7, pp 1791-1800, 2009
Scheduling in Heterogeneous Computing Environments for Proximity Queries
  Duksu Kim, Jinkyu Lee, Junghwan Lee, InSik Shin, John Kim, Sung-eui Yoon
  IEEE Transactions on Visualization and Computer Graphics, Vol. 19, No. 9, pp 1513-1525
Out-of-Core Proximity Computation for Particle-based Fluid Simulations
  Duksu Kim, Myung-Bae Son, Young J. Kim, Jeong-Mo Hong, Sung-Eui Yoon
  (To appear) Computer Graphics Forum, 2014

## Slide 89: Awards
Distinguished Paper Award
  Pacific graphics 2009
Student Stipend Award
  ACM I3D, Invited poster
Best CUDA Programming Award
  NVIDIA (Korea) CUDA coding contest 2010
Spotlight Paper
  IEEE TVCG, Sept., 2014

## Slide 90: Acknowledgements
Advisor, Sung-Eui Yoon
Committee members
SGLab. members and other co-workers

## Slide 91: Questions & Comments
Thank you!

## Slide 92: References
[Lawler 2002] A voxel-based parallel collision detection algorithm, O. S. Lawlor and V. K. Laxmikant, Super-computing, 2002
[Ize 2007] Asynchronous BVH construction for ray tracing dynamic scene on parallel multi-core architectures, T. Ize et al., Eurographics Symposium on Parallel Graphics and Visualization, 2007
[Wald 2007] On fast construction of sah-based bounding volume hierarchies, I. Wald, IEEE Symposium on Interactive Ray Tracing, 2007
[Tang 2009] Multi-core collision detection between deformable models, M. Tang et al., in SIAM/ACM Joint Conf. on Geometric and Solid & Physical Modeling, 2009
[Lee 2010] Simple and Parallel Proximity Algorithms for General Polygonal Models, Youngeun Lee et al, Journal of Computer Animation and Virtual Worlds, 2010
[Vassilev 2001] Fast cloth animation on walking avatars, T. Vassilev et al., Computer Graphics Forum (Eurographics), 2001
[Baciu 2002] Image-based techniques in a hybrid collision detector, G. Baciu and S. Wong, IEEE TVCG, 2002
[Govindaraju 2005] CULLIDE: Interactive collision detection between complex models in large environments using graphics hardware, EG. Workshop on Graphics Hardware, 2003
[Govindaraju 2005*] Collision detection between deformable models using chromatic decomposition," ACM Trans. on Graphics, 2005
[Lauterbach 2010] gProximity: Hierarchical GPU‐based Operations for Collision and Distance Queries, C Lauterbach et al., EG 2010
[GSSP 2010] GOSWAMI P., SCHLEGEL P., SOLENTHALER B., PAJAROLA R.: Interactive SPH simulation and rendering on the GPU. In Proc. of ACM SIGGRAPH/EGSymposium on Computer Animation, 2010

## Slide 93: References
[HKK 2007] HARADA T., KOSHIZUKA S., KAWAGUCHI Y.: Smoothed particle hydrodynamics on GPUs. In Proc. of Computer Graphics International, 2007
[IABT 2011] IHMSEN M., AKINCI N., BECKER M., TESCHNER M.: A parallel SPH implementation on multi-core CPUs. Computer Graphics Forum 30, 1, 2011

## Slide 94: Appendix

## Slide 95: Results
FPS