## Slide 1
Review for MinJae’s presentation (PairwiseNet)
Scalable Graphics, Vision & Robotics Lab
Collision distance
  Minimum distance between robot and nearest obstacle
Proposed a way to calculate distance between pairwise elements
  Useful for non-convex objects
  Generalizability (# robot, etc.)

## Slide 2: TerraPN: Unstructured Terrain Navigation using Online Self-Supervised Learning (IROS 2022)
Taegeun Yang
2023. 10. 30.
Scalable Graphics, Vision & Robotics Lab

## Slide 3: Introduction
Scalable Graphics, Vision & Robotics Lab

## Slide 4
Problem of Off-Road Navigation
Scalable Graphics, Vision & Robotics Lab
Off-Road environment ⇒ different surface characteristics
  Surface’s texture (traction)
  Bumpiness (vibration)
  Deformability (slip & stuck)
It affects the robot’s navigation
⇒ need to consider these features for planning

## Slide 5
How to address the problem? (Related works)
Scalable Graphics, Vision & Robotics Lab
Need to know the environment in advance
  Utilize vision information (e.g. RGB Camera)
Early studies
  Terrain classification using large image datasets
  Pre-defined traversability (e.g. water ⇒ untraversable)
⇒ However, do not account for robot’s properties and might misclassify
RUGD dataset

## Slide 6
How to address the problem? (Related works)
Scalable Graphics, Vision & Robotics Lab
Use Self-Supervised Learning
Data Collection
RGB Image, IMU data,
Odometry error, etc.
Navigation Cost
(High for untraversable area)
Cost Network
Sensor Input & Robot State
(RGB Image, Robot velocity, etc.)

## Slide 7
Contributions
Scalable Graphics, Vision & Robotics Lab
Novel method for training neural network using online self-supervised method
  Existing methods take a long time to re-train
Improve navigability cost representation using non-uniform sample patches
  Low inference times
Novel outdoor navigation algorithm
  Computes dynamically feasible collision-free trajectories
  DWA based algorithm

## Slide 8: Methods
Scalable Graphics, Vision & Robotics Lab

## Slide 9
Data Collection
Scalable Graphics, Vision & Robotics Lab
Autonomous Data Collection
  Moving along a rectangular path
  Moving in a serpentine trajectory
  Random motion
  Collision avoidance using DWA (Local planning)
  Cover all the [v, w] pairs
Training is started and performed online once sufficient data is collected (~6min)
Collecting Data
  RGB image, velocity, odometry, 6-DOF IMU, 3D LiDAR
  Calculate odometry error (LiDAR-based odometry – robot’s odometry) and IMU PCA variances
Grass
Concrete
Low speed
High speed
IMU PCA variances

## Slide 10
Overall Architecture
Scalable Graphics, Vision & Robotics Lab
Non-uniform image patches ⇒ Boundaries between surfaces (use Sobel edge detection)
Supervised Learning (Label: IMU PCA variances, Odometry error)
Cost map comes out the same size as the input RGB image

## Slide 11
Training
Scalable Graphics, Vision & Robotics Lab
Output (4 x 1)
Large image patches (2n x 2n, 4n x 4n, etc.) ⇒ resize to n x n
Linear & Angular velocities for the past n/2 instances

## Slide 12
Cost Calculation
Scalable Graphics, Vision & Robotics Lab
Network output
Navigability Cost
  Compute for each patch
W is a diagonal matrix with positive weights
  Weight for each element of the network output
High Cost
Low Cost

## Slide 13
Navigation Algorithm (DWA based)
Scalable Graphics, Vision & Robotics Lab
Dynamically feasible space ⇒
Optimization
Trajectory candidate
Image Plane

## Slide 14: Results
Scalable Graphics, Vision & Robotics Lab

## Slide 15
Results
Scalable Graphics, Vision & Robotics Lab
Evaluation Metric
  Success Rate
  Normalized Trajectory length
  Vibration Cost
  Mean Velocity
Inference Time
  Non-uniform image patches
  Baseline: OCRNet (uniform sampling)
  Reduces inference time by 47.27%
Scenario num

## Slide 16
Results
Scalable Graphics, Vision & Robotics Lab
High speed
Medium speed
Low speed

## Slide 17
Results
Scalable Graphics, Vision & Robotics Lab

## Slide 18: Conclusion
Scalable Graphics, Vision & Robotics Lab

## Slide 19
Conclusion
Scalable Graphics, Vision & Robotics Lab
Novel approach that uses self-supervised learning to identify the surface characteristics in complex outdoor environment
RGB images and robot’s velocity ⇒ IMU variations and odometry errors
Novel navigation algorithm that accounts for the surface cost
Limitations
  Cannot be applied on completely non-traversable surfaces (no training data)
  Cannot distinguish elevation changes in the same or similar surfaces (unavailability of depth)

## Slide 20: Questions
Scalable Graphics, Vision & Robotics Lab

## Slide 21: Quiz
Scalable Graphics, Vision & Robotics Lab

## Slide 22
Quiz
Scalable Graphics, Vision & Robotics Lab
Q1. Which of the following is not a "surface characteristic" as defined in the paper?
  1. Texture
  2. Color
  3. Bumpiness
  4. Deformability
Q2. Which learning technique was utilized in this paper?