## Slide 1
Final presentation:
Novel Learning and Sampling-based Motion Planner for High-Dimensional Robotic System
2020.12.8
Minh-Tuan Tran - Andrea Finazzi - Shinjeong Kim
Notes: 1

## Slide 2: Content
I. Introduction
II. Background and Relative work
III. Problem of Current Technique
IV. Proposed Method
V. Role of Members

## Slide 3
1. Motion Planning Problem definition & applications
2. Motion Planning for High-dimensional Robotic System
I. Introduction

## Slide 4
1. Motion Planning Problem definition & Applications
Motion Planning Problem
Given:
Free State Space (
Obstacle State Space ()
Init state (
Goal state (
Objective: Finding the collision-free trajectory from to .
Applications
Robot, Autonomous driving, etc.
collision-free
trajectory

## Slide 5
OpenAI RoboSchool : 50 DOF
2. Motion Planning for High-dimensional Robotic System
Humanoid Robot
Existing approaches did not succeed to manage high DOF
A high performance, novel approach for high-dimensional C-space is necessary.

## Slide 6
II. Background and Relative work
2. Deeply Informed Neural Sampling (DeepSMP)
4. Learned Latent Rapidly-exploring Random Trees (L2RRT)
1. RRT and RRT*
3. Motion Planning for High-dimensional robotic

## Slide 7
1. RRT and RRT*
Repeatedly expand tree until reach goal
Probabilistically complete
Not Optimal
a. Rapidly-exploring Random Tree (RRT)
b. RRT*
RRT + Connection refinement (Rewire)
Probabilistically complete
Asymptotically optimal
Low speed for complicated C-space

## Slide 8
2. Deeply Informed Neural Sampling (DeepSMP)
Encoder
Decoder
DeepSampler
DeepSampler
Encoder
Offline
Online
1.
2.
Contractive
AutoEncoder
Deep Sampler
Neural Sampling
(DeepSMP)
Speed was improved
Still not suitable for high dimensional problem

## Slide 9
RRT family : designed for mobile robots and low DOF robotic arms
  → not suitable for high-dimensional problem [1]
DeepSMP family : heavily rely on training data
  → e.g. DeepSMP : DeepSampler is trained by path from RRT*; also not suitable
3. Motion Planning for High-dimensional robotic
Previous methods cannot handle high-dimension.
Why?

## Slide 10
a. Latent Sampling-based Motion Planning (L-SBMP)
This model is divided into three parts:
Autoencoder
Network
4. Learned Latent Rapidly-exploring Random Trees (L2RRT)
Dynamics
Network
Collision
Checker
Notes: Autoencoder network to project the full dimensional state to lower state
Dynamic network to predict the next state in latent space (from 〖 𝒛〗_𝒕 to 𝒛 ̂_(𝒕+𝟏))
Checking collision network to identify whether 𝒛 ̂_(𝒕+𝟏) and 〖 𝒛〗_(𝒕+𝟏) is collision-free

## Slide 11
Differences compared to RRT
All operations are done on latent space (e.g. sampling, tree extension)
Use dynamics network to extend tree
Use collision check network to check if successive states are collision-free
Main Idea
Project all high-dimensional states to lower states and handle them
Then, high-dimensional problem can be handled (e.g. Humanoid robot)
4. Learned Latent Rapidly-exploring Random Trees (L2RRT)

## Slide 12
III. Problem of Current Technique
What is the main weak point of L2RRT
They use the random for dynamic network
Both of those loss function just use for checking whether latent predicted state is correct with real predicted state
So that, this approach just lead the dynamic network to learn the path of the random sampling like RRT in full state problem. So, it leads to the poor performance of L2RRT.

## Slide 13
III. Problem of Current Technique
What is the main weak point of DeepSMP:
DeepSMP don’t suitable for high-dimensional motion planning due to the lack of training data.

## Slide 14
IV. Proposed Method
1. Training L-SBMP
2. L2RRT*
3. Training DeepControlSampler
4. Predict Phase

## Slide 15
IV. Proposed Method
1. Training L-SBMP
The training data for the autoencoder and dynamics network consists of 10,000 environments, each with a trajectory of 10 successive states and control inputs.
The training data for the collision checking network consists of 25,000 environments, again with 10 pairs of states and a collision label.

## Slide 16
IV. Proposed Method
2. L2RRT*
We can add some more step in L2RRT to let it become L2RRT* which can provide the near-optimal path.
Step 2: With each iterator:
Step 2.1: Sampling the
Step 2.2: Choice the node nearest to
Step 2.3: Random the and use it as input of the trained dynamic network to predict
Step 2.4: Use the trained checking collision network to check collision-free of and
1
2
5
3
1

## Slide 17
IV. Proposed Method
2. L2RRT*
Step 2.5: check the radius near to find the neighbor. Assume that is the neighbor.
Step 2.6: computing the cost to move from to .
1
2
5
3
1
 | Current Cost (ccost) | Parent Node (pn) | Full state node
 | 4 |  | 
 | 11 |  | 
 | Current Cost (ccost) | Parent Node (pn) | Full state node
 | 4 |  | 
 | 11 |  | 

## Slide 18
IV. Proposed Method
2. L2RRT*
Step 2.5: check the radius near to find the neighbor. Assume that is the neighbor.
Step 2.6: computing the cost to move from to .
Step 2.7: if then use trained checking collision network to check collision-free of and .
1
2
5
3
1
 | Current Cost (ccost) | Parent Node (pn) | Full state node
 | 4 |  | 
 | 11 |  | 
 | Current Cost (ccost) | Parent Node (pn) | Full state node
 | 4 |  | 
 | 11 |  | 

## Slide 19
IV. Proposed Method
2. L2RRT*
Step 2.5: check the radius near to find the neighbor. Assume that is the neighbor.
Step 2.6: computing the cost to move from to .
Step 2.7: if then use trained checking collision network to check collision-free of and .
If there are collision-free then and =
1
2
5
1
2
 | Current Cost (ccost) | Parent Node (pn) | Full state node
 | 4 |  | 
 | 6 |  | 
 | Current Cost (ccost) | Parent Node (pn) | Full state node
 | 4 |  | 
 | 6 |  | 
Based on L2RRT* we can generate the near-optimal path

## Slide 20
IV. Proposed Method
3. Training DeepControlSampler
With the training data will be generated from the near-optimal path of L2RRT*
DeepControlSampler
ObsEncoder
encoder
decoder

## Slide 21
IV. Proposed Method
4. Predict Phase:
Use the trained deep control sampler to predict

## Slide 22
IV. Proposed Method
4. Predict Phase:
Predict by the trained dynamic network with and as the input.

## Slide 23
IV. Proposed Method
4. Predict Phase:
Check the collision of and with the trained checking collision network.

## Slide 24
IV. Proposed Method
4. Predict Phase:
With this model, We can utilize both of the efficiency of neural network-based predictor and the suitability for high-dimensional of L2RRT.

## Slide 25
V. Experiments
2. Training Process
4. Conclusions
1. Network Implementation
3. Evaluation

## Slide 26
1. Network Implementation
Environment:
TensorFlow v1 (cpu only) – Ubuntu 20.04 on DELL XPS 15
Network Structure:
Input (516):
  z_t, z_goal, z_Obs
Obstacle space preprocessor, from the CC network (pre-trained):
  5 dense layers with 50% dropout
Control network:
  5 dense layers with 50% dropout
Output (2):
  u_t

## Slide 27
2. Training Process: Training Data
We used L2RRT to generate trajectories for our model training.
100 problems: 70 for training, 20 for testing, 10 for evaluation
Training: ~500 rows
Testing: ~100 rows
Each best trajectory of training and test data is represented as a sequence of control inputs.
Z_0
z_goal
Z_t
u_t
For each best trajectory we gather multiple segments (rows):
{z_t, z_goal, z_obs, u_t}

## Slide 28
2. Training Process
We compare the predicted control and the target by a Mean Squared Error loss function:
The Adam Optimizer available in tensorflow is used to minimize the loss, with:
Learning rate: 0.0001

## Slide 29
3. Evaluation
Planning problem in a 32x32 pixels environment

## Slide 30
3. Evaluation
10 Evaluation Problems are solved with max 5000 samples.
5 Different Scenarios:
  Random control (L2RRT)
  25% learned control
  50% learned control
  75% learned control
  100% learned control
2 Evaluation Rates:
  Success Rate: number of solved problem at each iteration
  Cost Rate: normalized cost of the best solution at each iteration

## Slide 31
3. Evaluation: Success Rate
Samples
Solved problems

## Slide 32
3. Evaluation: Cost Rate
samples
Cost (normalized)

## Slide 33
3. Evaluation: Latent Space Visualization
Random
50% Learned
*Third problem of the evaluation set. 1000 samples limit

## Slide 34
4. Conclusions
First results are promising
We faced some limitations implementing and evaluating the algorithm:
  Training data at our disposal was limited.
  The complexity of the visual problem is limited.
  L2RRT* cannot be implemented without inverse kinematics, so optimal controls cannot be generated.

## Slide 35
4. Conclusions
Besides, we could further improve our model by:
  Improving the network design process.
  Generate new problems or augment the environment complexity (e.g. humanoid robot)
  Evaluate the effectiveness of collision checking in control generation, defining a collision rate parameter.

## Slide 36
Member | Role
Shinjeong Kim | Write the Introduction and Relative work sections Discuss about proposed method Discuss about implementation approach and results
Andrea Finazzi | Write the Experiment section Discuss about proposed method Implement and evaluate the experiments
Minh-Tuan Tran | Write the Proposed Method section Discuss about proposed method Discuss about implementation approach and results
VI. Role of Members