## Slide 1: Learning-based path planning for Aerial Multi-View Stereo Reconstruction
Team 3:
20204513 Hochang Lee
20194195 Truong Giang Khang

## Slide 2: Contents
Introduction
Related Works
Our Approach
Experimental Results
Future Works

## Slide 3: Introduction : Overview
Overview of 3D Aerial Scanning:
View selection
& Path planning
Captured 2D images
Images Captured
By drones
Reconstruction Pipeline
Reconstructed 3D model

## Slide 4: Introduction : View Selection & Path Planning
Our study is focused on :
  View selection and path planning: Choose View points and design an Optimal trajectory for drones to capture the images that can produce a high-quality 3D model
  Optimal trajectory: Minimum travel budget.
Optimal trajectory
2D images
Images Captured
By drones

## Slide 5: Introduction : 3D Reconstruction
3D Reconstruction: take a set of images as input and produce a 3D model of scene
Reconstruction Pipeline: COLMAP [1], DL-based [2]
Captured 2D images
Reconstructed 3D model
Reconstruction Pipeline

## Slide 6: Related Works : Common Approach
Explore-then-Exploit:
  Explore: Generate a coarse estimate of scene geometry and scene’s free space
    Fly drone along a default trajectory
    Put acquired images to 3D reconstruction pipeline
  Exploit: Use the acquired information above as input
    Design a utility function based on heuristic
    Generate trajectory by maximizing the utility function, respecting limited travel budget.
Initial trajectory
Coarse 3D model
Optimal trajectory
explore
exploit

## Slide 7: Related Works : Studies

## Slide 8: Our Approach : Overview
Existing approaches: Define heuristic scores between each view point and surface point
However, this approach may not be applicable in cases the surface is textureless or has occlusions
Therefore, instead of predefining the rules, we switch over to learning based approaches
Textureless
Occlusion

## Slide 9: Our Approach : Overview
Our Method: Predict “Reconstructability” score for each view by using a DL network
Reconstructability: Serve as a proxy for the accuracy of surface estimate produced by each view
  Similar to definition in [5]
  process subset of pixels instead of whole image for Multi-View Stereo (MVS)
   Accelerating MVS

## Slide 10
Define via ground truth depth and estimated depth by a reconstruction pipeline
where, indicates the pixel p of view image
  is the depth value estimated by 3D reconstruction pipeline
  is the ground truth depth value
  is the depth error which is related to reconstructability
  Define the reconstructability score via by a form of sigmoid function
  Hyperparameter normalize value of R in range (0,1)
Our Approach : Reconstructability Score

## Slide 11
Default Trajectory
Coarse 3D model
Grid view points
Path planning
Optimal trajectory and 3D reconstruction models
Explore
Exploit
Our Approach : Explore-then-Exploit
Heuristic Approach to Select View Points for Path Planning
- User Made Utility Function are used to guess how useful each view points are at discovering unknown surfaces

## Slide 12
Default Trajectory
Coarse 3D model
Grid view points
Path planning
Optimal trajectory and 3D reconstruction models
Explore
Exploit
Our Approach : Explore-then-Exploit
Depth + normal features rendered from coarse model
Images rendered from coarse model
Deep learning model
Predicted reconstructability score maps

## Slide 13
dcdcdcdcd
Coarse model
Depth + normal features rendered from coarse model
Images rendered from coarse model
Images rendered from GT model
Depth maps rendered from GT
Ground truth (GT) model
Depth maps estimated by COLMAP
Deep learning model
Predicted score maps
GT score maps
Training model
MSE loss
Our Approach : Training

## Slide 14
4 encoding blocks
4 decoding blocks for depth refinement
4 decoding blocks for Reconstructability prediction
Our Approach : Network Architecture - RecNet

## Slide 15
Optimize two losses simultaneously
  Loss 1: Depth reconstruction loss
    where, is refined depth, is ground truth depth
  Loss 2: Reconstructability prediction loss
    Use mean squared error loss between predicted map and ground truth
Total loss:
  where to control the influence of losses
Our Approach : Loss Function

## Slide 16: Our Approach : Path planning
Preprocessing
  Construct a ground set C – all possible camera poses around the scene.
    Each camera pose has 2 information: 3D Position and Camera Orientation
  Sample a set of surface points S on the coarse 3D model
Define an objective function for path planning from Reconstructability predictions:
  Camera poses , surface points
  Reconstructability at surface point induced by : ,
  is indicator for visibility of with

## Slide 17: Our Approach : Path planning
P is a trajectory, P = (p0, u0), (p1, u1),…,(pq, uq), where is camera position, is camera orientation
Find optimal path P*:
(CP C)
Similar to [3], use algorithm in [3] to solve this problem.

## Slide 18
Dataset for training and test:
  Simulation dataset - Training : 9 Scenes & Testing : 4 Scenes
  DTU dataset – Training : 97 scenes & Testing : 22 scenes
Experiment Results

## Slide 19
Reconstructability Prediction
  Compare with other baselines: Unet [7] and ConfNet [8]
  Evaluation metrics: MAE, RMSE
Unet [7]
ConfNet [8]
RecNet (Ours)
Experiment Results
 | MAE |  |  | RMSE |  | 
 | Simulation | DTU | Overall | Simulation | DTU | Overall
Unet | 0.258 | 0.080 | 0.173 | 0.140 | 0.037 | 0.091
ConfNet | 0.192 | 0.070 | 0.134 | 0.099 | 0.034 | 0.068
RecNet (Ours) | 0.181 | 0.071 | 0.128 | 0.082 | 0.034 | 0.059

## Slide 20
3D Modeling : Path Planning
  Compared with Sub-modular Coverage (Sub-Cov [3])
    Same path length budget
  Captured the set of images in ROS simulation
  Reconstruction Pipeline : CasMVSNet
Experimental Results
Constructed 3D Models with Coverage Paths
(a) Sub-Cov
(b) Ours

## Slide 21
Scenario 1 (Notre-Dame de Paris) |  | Scenario 2 (Alexander Nevsky) | 
Experimental Results
(a) Sub-Cov
(b) Ours
3D Modeling
  Qualitative results

## Slide 22
Experimental Results
 | Scenario1 |  |  | Scenario2 |  | 
 | Precision | Recall | F-Score | Precision | Recall | F-Score
Sub-Cov | 0.8172 | 0.7257 | 0.7687 | 0.8628 | 0.8836 | 0.8731
Ours | 0.8302 | 0.7922 | 0.8108 | 0.8734 | 0.9062 | 0.8895
3D Modeling
  Quantitative comparison
    Our method had better performance in Precision, Recall, and F-Score
  Sub-Cov scans the entire surface evenly, but our method scans more low-score surfaces.
    → Improvement in Modeling Performance
    → Effective for scanning complex structures
(a) Sub-Cov
(b) Ours
Precision : Percentage of reconstructed points that lie within threshold distance to the ground truth
Recall : Percentage ground truth points that lie within the threshold distance to the reconstructed points
F-Score : Mean between the Precision and Recall

## Slide 23
Conclusion
  Proposed a learning-based approach for path planning in Aerial 3D Scanning.
  Achieve a good performance for both reconstructability prediction and 3D reconstruction.
Future Works:
  Compare with more path planning methods
  Evaluate on the real-world scenes.
Conclusion

## Slide 24: References
https://colmap.github.io/
Yao, Yao, et al. "Mvsnet: Depth inference for unstructured multi-view stereo." Proceedings of the European Conference on Computer Vision (ECCV). 2018.
Roberts, Mike, et al. "Submodular trajectory optimization for aerial 3d scanning." Proceedings of the IEEE International Conference on Computer Vision. 2017.
Smith, Neil, et al. "Aerial path planning for urban scene reconstruction: a continuous optimization method and benchmark." (2018).
Hepp, Benjamin, Matthias Nießner, and Otmar Hilliges. "Plan3d: Viewpoint and trajectory optimization for aerial multi-view stereo reconstruction." ACM Transactions on Graphics (TOG) 38.1 (2018): 1-17.
Hepp, Benjamin, et al. "Learn-to-score: Efficient 3d scene exploration by predicting view utility." Proceedings of the European Conference on Computer Vision (ECCV). 2018.
Ronneberger, Olaf, Philipp Fischer, and Thomas Brox. "U-net: Convolutional networks for biomedical image segmentation." International Conference on Medical image computing and computer-assisted intervention. Springer, Cham, 2015.
Tosi, Fabio, et al. "Beyond local reasoning for stereo confidence estimation with deep learning." Proceedings of the European Conference on Computer Vision (ECCV). 2018.