## Slide 1
Hardware for GI
Hong-Yun Kim (EE)
KAIST (Korea Advanced Institute of Science and Technology)
Notes: 1
Hi, My name is Hong-Yun Kim and my major is an electronic engineering.
My lab is Multimedia VLSI Lab and
our lab’s interest is a designing and implementing a 3D Graphics processor for mobile devices.
So, my concern about global illumination is quite different from you, I mean CS students.
How to implement RT hardware with limited resources is my major interest in nowadays.
So, the topic I am going to tell you is Hardware for Global illumination.

## Slide 2: Contents
Basic Ray Tracing Flow (HW designer’s view)
Ray Tracing Implementations
  Software on CPUs
  Software on GPUs
  Dedicated Hardware
Hardware Issues on GPUs for Ray Tracing
Hardware Issues on Dedicated HW for Ray Tracing
Notes: The contents of this presentation is organized as these four.
Basic ray tracing flow (HW designer’s view)
Three implementations of Ray Tracing
  Software on CPUs
  Software on GPUs
  Dedicated Hardware
Hardware issues on GPUs for Ray Tracing
Hardware issues on dedicated hardware for ray tracing
Let’s start with basic ray tracing flow

## Slide 3: Basic Ray Tracing Flow
Ray Generation
  position(x,y,z), direction(dx,dy,dz)
    32bit floating point data  datapath width
Ray Traversal
  Kd-tree, BVH, etc
    Handling a data structure in HW  flexibility
Intersection Test
  Different computations for various primitives
  1 dot product + 3 squares
  2 dot products + 1 division for a plane
Notes: Basic ray tracing flow consists of 4 stages
Ray generation, Ray Traversal, Intersection test, and shading.
In Ray generation stage, position and direction of ray is generated,
and each data type is a vector having 3 FP components.
This determines a width of datapath.
In Ray Traversal stage, ray traverses through the space.
To improve a performance of traversing, data structures such as kd-tree, BVH are used.
So, hardware should handle these kind of data structures efficiently not to lose the benefits of data structure.
After then, Intersection test is performed between ray and primitives.
To perform the intersection, floating point calculation is required such as dot product, squares, divisions.

## Slide 4: Basic Ray Tracing Flow (cont’d)
Shading
  Fixed function
    Diffuse + specular + ∑reflection + ∑refraction
    L·N, V·N, ∑ (L·N, V·N), ∑ (L·N)
  Programmable shading
Notes: After all the color of additional rays at intersection point is determined,
Each color is combined to realistic image by the shading models.
Phong’s shading model is the most popular model, as you already know,
In each term of phong’s shading model, dot product is also used to calculate the intensity of each component
In addition, programmable shading is also required for ray tracing,
because programmable shading is already used in a rasterization hardware.
From this basic algorithm, lot’s of research has been performed

## Slide 5: FP units in Pixel Shader (0.13um)
Notes: In this slide, area of floating point unit is presented, that is used in pixel shader implemented by our Lab.
Generally used FP unit such as comparator, adder, multiplier, DP 4 unit are synthesized in 0.13um technology.
Each value is very large compared to the fixed point unit.
For example, fixed point DP3 including 3 multiplier and 2 adder has about 2000 gates.
But, in the case of FP, 2 input adder has about 3600 gates.
Gate count of FP unit has large portion of pixel shader as shown in this slide.
So, reducing these FP unit in HW is important and required ability for HW designer.

## Slide 6: Ray Tracing(RT) Implementations
Software on CPUs
  32 processor SGI machine (parker’99)
  Linux clusters-16 processors (Wald’02)
Software on GPUs
  RT on Programmable Graphics HW(Purcell’02)
  Photon Mapping on Graphics HW(Purcell’03)
  GPU Algorithm for Radiosity and Subsurface Scattering (Carr’03)
  Interactive k-D Tree on GPU RT(Horn’07)
Dedicated Hardware
  Ray Processing Unit for RRT(Woop’05)
Notes: Ray Tracing Implementation is classified into 3 types
according to the running level, which means that RT is running on Software or Hardware,
And running platform on CPUs or GPUs
First approach is a implementation with software on CPUs.
To achieve interactive frame rate, it requires many processor from 16 to 32.
Recent trends is to implement RT through shader program on GPUs
by exploiting a FP computing power and high programmabilitiy of latest GPUs
Mapping RT on Programmable Graphics HW
Photon mapping, other GPU algorithm, and kd tree traversing on GPU
The lack of GPU’s capability can be overcome by dedicated hardware,
So, it has been attempt to implement a dedicated HW.
Ray Processing Unit for Realtime Ray Tracing.

## Slide 7: Hardware Issues on GPUs for Ray Tracing
Recent trends of GPUs
  Highly programmability
  High capability of floating point computation
Mapping Ray Tracing to Graphics HW
  GPU as a streaming processor
  Divide RT algorithm into several kernels (using vertex/fragment program)
  Texture memory used to store data structures
Limits
  Preprocessing step to build the grid
  Building acceleration data structure for “dynamic scene”
Notes: Now, let’s look into Hardware issues on GPUs.
Recent GPUs have two features; highly programmability and FP computation
So, it has enough capability to implement a realtime RT.
To map RT algorithm to Graphics HW,
GPU is used as a streaming processor and
RT algorithm is divided into several kernel functions to execute in parallel by using shader program,
Data structure for traversing is stored in texture memory
But, it also has limitations;
Preprocessing to build the grid is required.and
Building data structure for dynamic scene is inefficient and requires more improvements
in Next presentation, how to map RT to GPU will be explained more detail,
Such as how to divide the RT algorithm and how to use texture memory for storing data structures and its operations

## Slide 8: Hardware Issues on Dedicated HW for Ray Tracing
Lack of capability of flow control in GPUs
Fully programmable dedicated HW
  Flexibility(CPU) + data parallelism(GPU)
  Design decisions for designing a dedicated HW
    thread, control flow & recursion, dedicated traversal unit, memory access, scalable design
  Proposed instruction set & register
Limits
  Creating & maintaining spatial index structures for highly dynamic scene
  Inefficient computing anti-aliasing(AA)
Notes: In this slide, Hardware issues on dedicated HW is presented.
Although its programmability is increased, it still has insufficient to handle loop or recursion of RT alrorithm
So, Fully programmable dedicated HW was proposed
by exploiting both CPU’s flexibility of programming and GPU’s data parallelism
There are lot’s of design decisions for design; for example, how to handle thread, control flow & recursion, memory access, scalable design
And to improve the performance of RT HW instruction set and register is proposed.
Even in dedicated HW, handling data structures for highly dynamic scene is difficult problem.
And it is also inefficient to compute anti-aliasing
In next presentation, how to combine two advantages of CPU and GPU, how to decide the architecture,
and proposed Instruction set & register will be explained