## Slide 1
Hardware for GI
Hong-Yun Kim
KAIST (Korea Advanced Institute of Science and Technology)
Notes: 1

## Slide 2: Recent GPUs
High flexibility on programmability
High computing power of floating point
Considered as a stream processor
Attempts to implement GI algorithm on GPU

## Slide 3: I will cover …
GI on GPU
  Ray Tracing on Programmable Graphics Hardware [02’SIGGRAPH-Timothy J. Purcell][1]
  Photon Mapping on Programmable Graphics Hardware [03’GH-Timothy J. Purcell][2]
  GPU Algorithms for Radiosity and Subsurface Scattering [03’GH-Nathan A. Carr][3]
  Interactive k-D Tree GPU Ray Tracing [07’I3D- Daniel Reiter Horn][4]

## Slide 4: I will cover …
Ray Tracer on a Dedicated Hardware
  RPU: A Programmable Ray Processing Unit for Realtime Ray Tracing [05’SIGGRAPH-Sven Woop]

## Slide 5: Contents
How Ray Tracing can be mapped to GPU ? [1]
  Key Idea
  Results
  Pros. & Cons.
How advanced algorithms are implemented ?
  Photon Mapping on GPU [2]
  Radiosity on GPU [3]
  Subsurface Scattering on GPU [3]
  K-D Tree Traversing on GPU [4]

## Slide 6: How Ray Tracing can be mapped to GPU ?
Streaming Ray Tracer
Mapping to fragment program
Ray Tracing kernels
  Eye Ray Generator
  Traverser
  Intersector
  Shader
Implementation

## Slide 7: Streaming Ray Tracer
Streaming Model
Streaming Ray Tracer
Eye Ray
Generator
Traverser
Intersector
Shader
Pixel color
Materials
Hits
Camera
Screen Pixels
Rays
Grid
(Ray, Voxel)
Triangles
Kernel
Global memory
Input record stream
Kernel
Output record stream

## Slide 8: Mapping to Fragment Program
Fragment Processing
  Rich Instruction Set (in 2002)
  Floating Point (arithmetic, texture memory)
Purcell’s slide of Ray Tracing on a Stream Processor(2004)

## Slide 9
Kernel
(Fragment Shader)
Memory (Textures)
Operations
Frame
Buffer
Screen
aligned
Quad
Fragment
Output
Data
(Texels)
Feedback !

## Slide 10: Ray Tracing Kernels
Eye Ray Generator
  Inputs :
    Camera parameters (view point & direction)
    Screen pixel
  Output : Eye ray for each pixel
  Additional techniques :
    Ray-Scene intersection check to terminate useless rays
Eye Ray Generator
Traverser
R-T Intersector
Shader

## Slide 11: Ray Tracing Kernels
Traverser
  Searching for voxels containing triangles
Eye Ray Generator
Traverser
R-T Intersector
Shader

## Slide 12: Ray Tracing Kernels
Intersector
  Performing ray-triangle intersection test
    Inputs : ray-voxel pairs
    Output : ray-triangle(R-T pair) hits
      Hit  passing R-T pair to shading stage
      Miss  go to traversing stage
  Data structure formats
    Integer offset : 1-component FP texture
    Triangle vertex texture : 3 FP RGB textures
Eye Ray Generator
Traverser
R-T Intersector
Shader

## Slide 13: Code for R-T Intersection
Load vertices of the triangle
R-T Intersection test
Validity Test
Return Hit position
Eye Ray Generator
Traverser
R-T Intersector
Shader

## Slide 14: Ray Tracing Kernels
Shader
  Evaluating the color contribution of a given ray at the hit point
    Inputs : hit point & hit triangle id
    Outputs : color
  By choosing different shading rays,
    Shadow Casting (eye ray only)
    Ray Casting (shadow ray only)
    Whitted Ray Tracing
      (reflection/refraction/shadow rays)
    Path Tracing (randomly scattered from surface)
Eye Ray Generator
Traverser
R-T Intersector
Shader

## Slide 15: Results of Several Shaders
Eye Ray Generator
Traverser
R-T Intersector
Shader

## Slide 16: Implementation Issues-1
Efficiency of Ray Tracing depends on loop
  Traversing a data structure
  Testing for an intersection of a ray-triangles
To handle loop efficiently
  Multipass Architecture (with stencil buffer)
  Branching Architecture
Nowadays, this is not a issue !
PS ver | 2.0 | 2.0a | 2.0b | 3.0 | 4.0
Dynamic flow control | No | No | No | 24 | Yes

## Slide 17: Implementation Issues-2
How to reduce the # of passes ?
  Strategies for nesting loops (Traversing/R-T Test)
    simplest algorithm :
      Step through voxels until ray encounters a voxel containing triangles
      Then, perform R-T intersection test
    More efficient algorithm : (on SIMD machine)
      Treversing or Intersection are performed simultaneously
      Not wait until R-T intersection test is done

## Slide 18: Results – Scene Statistics
V : average # of voxels pierced by a ray
T : average # of triangles intersected by a ray
S : average # of shading calculations per ray
Rendered at 1024x1024 pixels

## Slide 19: Results - Bandwidth Distribution
Left bar : Instruction
Right bar : bandwidth
Most of bandwidth & instruction is used for intersection/traverser kernels !!
Branching arch. consumes less BW than multipass arch.

## Slide 20: Pros. And Cons.
Pros.
  Compute limited not bandwidth limited  allowing high R-T test up to available BW
  Storing all the scene triangles on GPU  eliminating CPU-GPU bottleneck
Cons.
  Preprocessing step to build the grid
  Simple uniform grid  fail for empty space
  Large texture memory (200~300MB)

## Slide 21: How advanced GI algorithms are implemented ?
Photon Mapping [2]
Radiosity [3]
Subsurface Scattering [3]
K-D Tree Traversing [4]

## Slide 22: Photon Mapping Review [2]
Photon tracing
  Emission, scattering, storing into kd-tree
  Similar to ray tracing
Rendering
  Ray tracing for direct illumination
  Photon map visualization
    Indirect bounce
(Purcell’s slide)
(Purcell’s slide)

## Slide 23: System Flow for Rendering
Photon tracing (geometry & lighting changes)
Ray Tracing/Compute Radiance (every frame)
These were performed CPU.
How to handle these on GPU?

## Slide 24: Two Challenges for GPUs
Constructing a spatial data structure
Adaptive nearest neighbor search (kNN)
  Noise vs. blur
(Purcell’s slide)
(Purcell’s slide)
< Photon Map >
< Radiance Estimation>

## Slide 25: Algorithmic Changes for the GPU
Balanced kd-tree
  Compact storage of photons
  Efficient
  O(log n) search
Priority queue
  Nearest neighbor search
Use uniform grid
  K-d tree requires random access write to construct
No priority queue
  KNN-grid method
[ On CPU ]
[ On GPU ]

## Slide 26: Constructing the Photon Map (by Fragment Program)
Goal : indexing photons by grid cell
How to ?
  Sorting them by cell
  Find the index of the first photon in a cell (using binary)
Problems for sorting on GPU
  Requires to write to arbitrary locations  limits the ability of parallel computing of GPU
Solutions !
  Using Bitonic Merge Sort  output routing is known in advance

## Slide 27: Bitonic Merge Sort
1
3
2
4
7
6
8
5
2
3
1
4
7
5
8
6
3
2
4
1
7
5
8
6
3
7
4
8
2
5
1
6
3
8
4
7
2
6
1
5
1
2
3
4
5
6
7
8
3
8
7
4
5
6
1
2
O(log2 n) rendering passes !!
Purcell’s slide
Notes: <number>

## Slide 28: Binary Search for Finding the First Photon
v5
Grid cell searches for self in photon list
  If none, find first element in next cell
    Empty grid cells waste compute
  Log(n) + 1 steps
v0
v0
v2
v2
v5
v0
v5
Sorted
Photon List
v0
v0
v2
v2
v2
v0
v5
v0
v0
v2
v2
v5
v0
v0
v0
v2
v2
v2
v0
v5
v0
v0
v2
v2
v2
v0
v5
v2
v5
v2
v5
v5
Searching for first v5 photon
initialize
step 1
step 2
step 3
step 4

## Slide 29: Resultant Textures by Bitonic Merge Sort
Uniform Grid texture : index of the first photon
Photon List texture : list of photon indices (sorted by grid cell)

## Slide 30: Constructing the Photon Map (by Vertex Program )
Problem of Bitonic Merge Sort
  O(log2n) rendering passes are required !
Propose) Use vertex program !
  Providing a mechanism for drawing a glPoint to an arbitrary location in a buffer  To construct a photon map in a single pass
What about many-to-one routing ? (many photons are stored in one grid cell)
Propose) Use stencil buffer
  How to?

## Slide 31: Stencil Routing
Limit photon count per grid cell
  Pre-allocate grid cell space
Draw photons as points
  Vertex program computes grid cell
Stencil buffer controls location within cell
Single rendering pass
Notes: <number>

## Slide 32: Stencil Routing
Fix each grid cell size to n2 pixels
Draw fat points to cover each fat cell
  glPointSize(n)
Vertex ( photon_pos )
Vertex Program
Flattened Grid
4 pixels

## Slide 33: Stencil Routing
Control location written to with stencil
  Pass when stencil is n2 -1
  Stencil always increments
  Location written depends on draw order
Vertex ( photon_pos )
Vertex Program
Flattened Grid
1 pixel
Stencil
4 pixels
Stencil Values
0
1
2
3
1
2
3
4
0
1
2
3
0
1
2
3

## Slide 34: Two Challenges for GPUs
Constructing a spatial data structure
Adaptive nearest neighbor search (kNN)
  Noise vs. blur
(Purcell’s slide)
(Purcell’s slide)
< Photon Map >
< Radiance Estimation>

## Slide 35: K Nearest Neighbor search (kNN)
Needs to locate the nearest photons  to estimate radiance at a given surface
kNN-grid method
  Developed for finding k-nearest neighbors to a sample point in a uniform grid
  Operations
    Explore all of the photons in the grid containing a sample point
    Rejected if it is outside of predefined max radius
    All grid cells are explored in concentric set centered about sample point
Notes: <number>

## Slide 36: kNN-grid Algorithm (purcell’s slide)
Finds all photons within a sphere centered about sample point
May locate more than requested k-nearest neighbors  more blur, but image quality is not suffered from this
6
sample point
photons in estimate
candidate photon
Want a 4 photon estimate

## Slide 37: Results – Image Quality
@ 512x384, 5K photons
@ 512x384, 16K photons
@ 512x512, 65K photons

## Slide 38: Results – GPU Rendering Time
Majority rendering time is
  Performing the radiance estimate
Stencil Routing is better than Bitonic Sort

## Slide 39: Results – Instruction Use
At least 20 arithmetic operations for every texture access
  Converting the coordinate of 1D to 2D texture’s
  Implements simple calculations with extra inst (Lack of integer arithmetic OPs)
  Packing/Unpacking for multiple outputs of the radiance estimate (limited output form to 128bit)

## Slide 40: Pros. & Cons.
Pros.
  Proposed method entirely on GPU
    Constructing a grid-based photon map
    Searching for k-nearest neighbors
  Compute bound algorithm, not memory BW
Cons.
  Fragment Program Instructions Set 1) address conversion 2) simulating integer arithmetic 3) packing/unpacking
  Texture readback & copy  performance penalty
  High resolution of the grid for complex scene

## Slide 41: How advanced GI algorithms are implemented ?
Photon Mapping [2]
Radiosity [3]
Subsurface Scattering [3]
K-D Tree Traversing [4]

## Slide 42: Radiosity [3] Overview (Carr’s slide)
Goal : solve radiosity matrix KB=E on GPU
Use Jacobi iteration for solution
  Converges slower than Gauss-Seidel
  But more parallelism than Gauss-Seidel
Use natural representation
  Matrix is 2D texture, vectors are 1D textures

## Slide 43: Jacobi vs. Gauss-Seidel (Carr’s slide)
Jacobi iteration
  Classical: Bi(k+1) = Ei – ji Kij Bj(k)
  Dependence free: Bi(k+1) = E – KB(k) + B(k)
Gauss-Seidel
  Needs dependence: Bi = Ei – ji Kij Bj
  But converges 2x Jacobi!
GPU Gauss-Seidel
  n passes (Kruger & Westermann S03)
GPU Jacobi
  n/254 passes (unrolled)
Kii = 1
N : # of patches, 254 : Block size

## Slide 44: Radiosity: Details (Carr’s slide)
Each Jacobi iteration requires multiple passes due to fragment shader instruction limits
First: (passes)
Finally: (1 pass)
Each output element is computed in parallel
Could interpolate to vertices on GPU

## Slide 45: Results (Carr’s slide)
CPU: Athlon 2800+
  Gauss-Seidel
  40 iter/s, 190M flops
  Bandwidth-limited
GPU: GFFX 5900 Ultra
  Jacobi
  30 iter/s, 141 MFLOPS
  Compute-limited
GPU
CPU

## Slide 46: Pros. & Cons.
Pros.
  Each output element is computed in parallel
Cons.
  Currently slower than on CPU
    But, compute speed increases faster than BW
  Better organization needed for complex scenes
    Could also make interpolating results easier
    Might improve performance (caching)

## Slide 47: I will cover these in next time
GI on GPU
  Ray Tracing on Programmable Graphics Hardware [02’SIGGRAPH-Timothy J. Purcell][1]
  Photon Mapping on Programmable Graphics Hardware [03’GH-Timothy J. Purcell][2]
  GPU Algorithms for Radiosity and Subsurface Scattering [03’GH-Nathan A. Carr][3]
  Interactive k-D Tree GPU Ray Tracing [07’I3D- Daniel Reiter Horn][4]

## Slide 48: I will cover these in next time
Ray Tracer on a Dedicated Hardware
  RPU: A Programmable Ray Processing Unit for Realtime Ray Tracing [05’SIGGRAPH-Sven Woop]