## Slide 1
Hardware Design
for Traversing a KD-Tree
Hong-Yun Kim
KAIST (Korea Advanced Institute of Science and Technology)
Notes: 1

## Slide 2: Goal
HW design for fast traversal of KD-Tree
Target System Architecture
  Multiple scalar PEs(processing elements)
  Multi-thread architecture (SIMT)
PE
PE
PE
PE
PE
PE
PE
PE
Texture $ L2
Texture $ L1
Texture $ L1
Bandwidth

## Slide 3: KD-Tree Data Structure
D
I
H
E
K
J
B
F
M
L
G
O
N
C
A
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
…
Texture memory
PE
PE
PE
PE
PE
PE
PE
PE
Frequent accesses !!
3D Graphics Core

## Slide 4: Problem of Traversing KD-Tree
For every rays (primary, secondary rays)
Pop the node from stack
Clipping ray
to the end/start point
Start traversing
in KD-tree
Find the leaf node
Store far node to stack
Load list of triangles
in the leaf node
Intersection test
 valid ?
Read color/normal at the intersection point
Yes
No
Hardware limitation !
Memory bottleneck !
Memory bottleneck !

## Slide 5: To improve the performance …
These problems should be resolved !
  Frequent texture memory accesses
  Low hit rate of the texture $
  Large amount of redundant traversal steps
Let’s estimate the performance of ray tracer for a mobile device

## Slide 6: Simple Calculations- (1/2)
Target environments
  Resolution : QVGA (320x240)
  # of primary rays : α rays
  # of secondary rays : ß rays
  Cost(traversal) : C cycles
  Texture $ hit rates : Rhit
  Clock frequency : 100 MHz
  # of traversal step per ray : H steps
  Required time / frame : T seconds
320
240
# of rays
Cycle time for reading one node

## Slide 7: Simple Calculations-(2/2)
Ideal case (L1 $ Hit rate = 100 %)
  α = 4, ß = 3, C = 10, H =10 (1024 triangles)
  T = 92 ms  10.8 FPS
Worst case (L1 $ Hit rate = 0%)
  α = 4, ß = 3, C = 10, H =10 (1024 triangles)
  T = 92x10 ms  1.1 FPS
Packet & fast traversing algorithm(FTA)
  α = 4, ß = 3, C = 10/4(rays), H =10/3(FTA)
  T = 92x(1/4)x(1/3) ms  130.0 FPS

## Slide 8: How to improve ?
We want to improve these factors
  Cost(traversal) : C cycles
  Texture $ hit rates : Rhit
  # of traversal step per ray : H steps
How to reduce C ?
  By using multi-level cache architecture
How to reduce Rhit ?
  By packetizing rays (to exploit the SIMD/ SIMT)
  By adjusting a order of shooting ray
How to reduce H ?
  By introducing faster traversal algorithm

## Slide 9: Adjusting an order of shooting ray ?
A
B
C
D
E
F
G
…
Texture memory
PE
PE
PE
PE
PE
PE
PE
PE
A
C
E
G
PE
PE
PE
PE
PE
PE
PE
PE
A
C
B
D
B
C
D
D
E
F
F
G
H
H
I
J
H
I
J
K
Texture $
From the fact,
the closer rays,
the more coherent !

## Slide 10: What if ray is shoot in this order ?
A
B
C
D
E
F
G
…
Texture memory
PE
PE
PE
PE
PE
PE
PE
PE
A
C
B
D
PE
PE
PE
PE
PE
PE
PE
PE
A
C
B
D
B
C
D
D
E
F
D
G
K
K
F
J
H
I
J
K
Texture $
More cache hit !!
More coherent
Between rays !!

## Slide 11: Benefits
High hit rate of the texture $
   Rendering time decreases  FPS increases !!

## Slide 12: How to implement ?
Simple ray tracer (from the internet)
  Analysis of the code is already done
Modifications to the original code
  I will implement various methods for comparisons
    row-by-row
    Z curve
    H curve
    Hilbert curve
    βΩ curve

## Slide 13: Various Curves
From the yoon’s paper

## Slide 14: Schedule
11/ 2 week
11/ 3 week
11/ 4 week
12/ 1 week
12/ 2 week
12/ 3 week
09/ 2 week
09/ 4 week
10/ 1 week
10/ 3 week
10/ 4 week
11/ 1 week
Studying base of ray tracing
Analyzing the simple ray tracer code
Surveying traversing algorithms
Analyzing the order of ray shooting
Optimizing a SIMT architecture
Branch handling
Optimized # of PE / architecture
C++ coding / simulations
RTL coding / synthesis
Reducing a redundant traversal steps
Modification of previous algorithms
Exploiting hardware resource for stack

## Slide 15: NVIDIA TESLA
Unified graphics and computing architecture