## Slide 1
CS380: Computer Graphics
Texture Mapping
Sung-Eui Yoon
(윤성의)
Course URL:
http://sglab.kaist.ac.kr/~sungeui/CG
Notes: 1

## Slide 2: Class Objectives
Texture mapping overview
Texture filtering
Various applications of texture mapping
Related chapter of my book
  Chapter 9 “Texture”

## Slide 3: Texture Mapping
Requires lots of geometry to fully represent complex shapes of models
Add details with image representations
Excerpted from MIT EECS 6.837, Durand and Cutler

## Slide 4: The Quest for Visual Realism

## Slide 5: Texture Mapping
From MMO-champion

## Slide 6: Texture Maps in OpenGL
Specify normalized texture coordinates at each of the vertices (u, v)
Texel indices (s,t) = (u, v)  (width, height)
glBindTexture(GL_TEXTURE_2D, texID)
glBegin(GL_POLYGON)
glTexCoord2d(0,1); glVertex2d(-1,-1);
glTexCoord2d(1,1); glVertex2d( 1,-1);
glTexCoord2d(1,0); glVertex2d( 1, 1);
glTexCoord2d(0,0); glVertex2d(-1, 1);
glEnd()
(x4,y4) (u4,v4)
(x1,y1) (u1,v1)
(x2,y2) (u2,v2)
(x3,y3) (u3,v3)

## Slide 7: Wrapping
The behavior of texture coordinates outside of the range [0,1) is determined by the texture wrap options.
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_S, wrap_mode )
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_T, wrap_mode )
GL_CLAMP
GL_REPEAT
Notes: How do we get repeat?

## Slide 8: Linear Interpolation of Texture Coordinates
Simple linear interpolation of u and v over a triangle in a screen space leads to unexpected results
  Distorted when the triangle’s vertices do not have the same depth
  Perspective-correct interpolation (interpolation in the object space) is implemented

## Slide 9: Sampling Texture Maps
The uniform sampling pattern in screen space cooresponds to some sampling pattern in texture space that is not necessarily uniform
Screen space
Texture space
x
y
s
t

## Slide 10: Sampling Density Mismatch
Sampling density in texture space rarely matches the sample density of the texture itself
Oversampling
(Magnification)
Undersampling
(Minification)

## Slide 11: Handling Oversampling
How do we compute the color to assign to this sample?
texture
sample

## Slide 12: Handling Oversampling
How do we compute the color to assign to this sample?
Nearest neighbor – take the color of the closest texel
texture

## Slide 13: Handling Oversampling
How do we compute the color to assign to this sample?
Nearest neighbor – take the color of the closest texel
Bilinear interpolation
texture

## Slide 14: Visual Comparison
Mag. filter: nearest
Min. filter: linear
Mag. filter: linear
Min. filter: linear
Mag. filter: linear
Min. filter: mipmap
Original texture

## Slide 15: Undersampling
Details in the texture tend to pop (disappear and reappear)
  Mortar (white substances) in the brick
High-frequency details lead to strange patterns
  Aliasing

## Slide 16: Spatial Filtering
To avoid aliasing we need to prefilter the texture to remove high frequencies
  Prefiltering is essentially a spatial integration over the texture
  Integrating on the fly is expensive: perform integration in a pre-process
Samples and their extents
Proper filtering removes aliasing

## Slide 17: MIP Mapping
MIP is an acronym for the Latin phrase multium in parvo, which means "many in one place"
  Constructs an image pyramid
  Each level is a prefiltered version of the level below resampled at half the frequency
While rasterizing use the level with the sampling rate closest to the desired sampling rate
  Can also interpolate between pyramid levels
How much storage overhead is required?
Notes: 4/3 = epsilon_{i=0} (1/4)^I = 1/(1 – ¼) = 4/3

## Slide 18: Storing MIP Maps
One convenient method of storing a MIP map is shown below
  It also nicely illustrates the 1/3 overhead of maintaining the MIP map

## Slide 19: Finding the MIP Level
Use the projection of a pixel in screen into texture space to figure out which level to use

## Slide 20: Summed-Area Tables
Another way performing the prefiltering integration on the fly
Each entry in the summed area table is the sum of all entries above and to the left:
What is the sum of the highlighted region?
Divide out area (y1 – y0)(x1 – x0)

## Slide 21: Summed-Area Tables
How much storage does a summed-area table require?
Does it require more or less work per pixel than a MIP map?
Can be implemented in a fragment shader
Created by Denny
Notes: Less storage, but more resolution
more work – 4 texture fetches – still have to do size estimation
box filter
can see the results of isotropic filtering

## Slide 22: Texture Filtering in OpenGL
Automatic creation gluBuild2DMipmaps(GL_TEXTURE_2D, GL_RGBA, width, height, GL_RGBA, GL_UNSIGNED_BYTE, data)
Filtering
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MAG_FILTER, filter )
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MIN_FILTER, filter ) where filter is: GL_NEAREST GL_LINEAR GL_LINEAR_MIPMAP_LINEAR GL_NEAREST_MIPMAP_NEAREST GL_NEAREST_MIPMAP_LINEAR GL_LINEAR_MIPMAP_NEAREST
inter-level
intra-level

## Slide 23: Uses of Texture Maps
Texture maps are used to add complexity to a scene
  Easier to paint or capture an image than geometry
Model light
Model geometry, etc
One of key techniques to overcome various problems of rasterization techniques!

## Slide 24: Modeling Lighting
Light maps
  Supply the lighting directly
  Good for static environments
Projective textures
  Can be used to simulate a spot light
  Shadow maps
Environment maps
  A representation of the scene around an object
  Good for reflection

## Slide 25: Light Maps in Quake
Light maps are used to store pre-computed illumination
 | Texture Maps | Light Maps
Data | RGB | Intensity
Resolution | High | Low
Light map image by Nick Chirkov
Textures Only
Textures & Light Maps

## Slide 26: Projective Textures
Treat the texture as a slide in a projector
  A good model for shading variations due to illumination (cool spotlights)
Projectors work like cameras in reverse
  Camera: color of point in scene  color of corresponding pixel
  Projector: color of pixel  color of corresponding point in the scene

## Slide 27: Shadow Maps
Depth map from light
Depth map from eye
Point in shadow
visible to the eye, but not visible to the light
Use the depth map in the light view to determine if sample point is visible

## Slide 28: Environment Maps
Simulate complex mirror-like objects
  Use textures to capture environment of objects
  Use surface normal to compute texture coordinates
View
Spherical env. map

## Slide 29: Environment Maps - Example
T1000 in Terminator 2 from Industrial Light and Magic

## Slide 30: Cube Maps
Maps a viewing direction b and returns an RGB color
  Use stored texture maps

## Slide 31: Cube Maps
Maps a viewing direction b and returns an RGB color
  Assume b = (x, y, z),
- Identify a face based on magnitude of x,y,z
-For the right face, compute texture coord. (u,v)
u = (y+x)/(2x)
v = (z+x)/(2x)
Notes: Parameterize a line P(t) starting at P0(0, 0, 0) in the direction of (x, y, z)
Let the right face to be x=1 plane. Then, the intersection point, (1, x’, y’) become (tx, ty, tz).
So, x’ = y/x, y’ = z/x, where x’ and y’ ranges between -1 and 1).
After mapping them to (0, 1), we got the above equations.

## Slide 32: Environment Maps - Problems
Expensive to update dynamically
Not completely accurate
  One of main reason that Cars (Pixar movie of 2006) used ray tracing
Reflection of swimming pool is wrong
images from NVIDIA
Notes:   Not completely accurate
  Assumes that all reflected rays begin from the same point and all objects in the scene are the same distance from that point
  May not represent the “near field” very well

## Slide 33: Environment Maps - Problems
Expensive to update dynamically
Not completely accurate
  One of main reason that Cars (Pixar movie of 2006) used ray tracing
Notes:   Not completely accurate
  Assumes that all reflected rays begin from the same point and all objects in the scene are the same distance from that point
  May not represent the “near field” very well

## Slide 34: Modeling Geometry
Store complex surface details in a texture rather than modeling them explicitly
Bump maps
  Modify the existing normal
Normal maps
  Replace the existing normal
Displacement maps
  Modify the geometry
Opacity maps and billboards
  Knock-out portions of a polygon using the alpha channel

## Slide 35: Bump Mapping
Modifies the normal not the actual geometry
  Texture treated as a heightfield
  Partial derivatives used to change the normal
  Causes surface to appear deformed by the heightfield
+
=

## Slide 36: More Bump Map Examples
Note that silhouette edge of the object not affected!
+
=

## Slide 37: Normal Mapping
Replaces the normal rather than tweaking it

## Slide 38: Displacement Mapping
Texture maps can be used to actually move surface points
The geometry must be displaced before visibility is determined
  Is this easily done in the graphics pipeline?

## Slide 39: Opacity Maps
Use the alpha channel to make portions of the texture transparent
alpha channel
RGB channels

## Slide 40: Billboards
Replace complex geometry with polygons texture mapped with transparent textures

## Slide 41: 3D or Solid Textures
Solid textures are three dimensional assigning values to points in 3 space
  Very effective at representing some types of materials such as marble and wood
Generally, solid textures are defined procedural functions rather than tabularized functions as used in 2D

## Slide 42: Class Objectives were:
Texture mapping overview
Texture filtering
Various applications of texture mapping

## Slide 43: Next Time
Visibility and ray tracing

## Slide 44: Homework
Go over the next lecture slides before the class
No more video abstract submissions on June

## Slide 45: Figs

## Slide 46
(x4,y4) (u4,v4)
(x1,y1) (u1,v1)
(x2,y2) (u2,v2)
(x3,y3) (u3,v3)

## Slide 47
Screen space
Texture space
x
y
u
v

## Slide 48: Handling Oversampling
texture
sample
Bi-linear interpolation

## Slide 49: Summed-Area Tables
Original texture
Summed-area table

## Slide 50: Shadow Maps
Depth map from light
Depth map from eye

## Slide 51: Environment Maps
View
Spherical env. map